## Slide 1: Robot Joint/Dynamic Control
Meow: This will just be a summary of the key concepts. Please watch lecture slides for more details on the concepts.
These two cats seem to have claimed ownership of my house.
Notes: A lot of the most important content has been covered by the lecture. Especially the formulas. The formulas are very complicated and will require time to go through. So, refer students to watch the lecture and have a go at attempting the lab task in particular.
Solutions will be released next week for it.
There may be a question similar to it in quiz 2 next Friday.

## Slide 2: What do we know so far?
Lets suppose we want the robot to move to a specific pose to pick up some object.
We can:
  Figure out the IK solution to determine the joint angle positions necessary for the robot to reach that required pose.
But how do we figure out how to control each motor to reach desired joint angles?
Notes: We know how to calculate the pose given joint positions
We know how to calculate the joint positions given a pose
  But this is still very hard. Do able for simple for the simple example presented in the lectures
The next step is figuring out how to actually control the physical motor or rotational actuator to make it reach the desired joint positions

## Slide 3: Robot-Joint Control
Robots are typically controlled by actuators:
  Hydraulic
  Pneumatic
  Electric
The UR5e has an electric rotary actuator.
  Converts input electric current to output torque
  Converts input voltage to output rotational velocity
Notes: Robots are controller by actuators and there are different types
  Hydraulic
  Pneumatic
  Electric
Actuators can be linear or rotational.
The ur5e is consisted of electric rotary actuators, which
  Converts an input electric current to output torque or
  Voltage to output rotational velocity. However, you want to look at it

## Slide 4: Robot-Joint Control Cont. A very simplified diagram
Joint control Algorithm
Actuator
Position Sensor
Desired Joint Angle Position
Actual Joint Angle Position
PWM
Torque
Notes: This diagram shows a very very simplified version of the fundamentals of how robot joint control works. We input the desired joint angle and then the joint angle control algorithm handles the rest. It sends PWM signals to the actuator to rotate it. We also have a position sensor which provides us with feedback of the actual joint position of the actuator.
The position sensor is very important as this is what is used to create the control algorithms. For example a PID.

## Slide 5: Robot-Dynamic Control
It’s a bit more complicated than what the diagram on the previous slide represents.
The physical world applies some effect to each of the links on the robot that must be considered in the control algorithm
For example: When the robot is stationary, a constant torque must be applied to each motor to help hold the position. Otherwise it will just fall down!
Notes: So how do we figure out what electrical signals to send to it?
Well first we need to figure out what torque to send to it, and then use that to figure out the electrical signals required!
The diagram is heavily simplified. We have things like gravity and the Coriolis force acting on the robot.

## Slide 6: Robot-Dynamic Control
Other forces such as gravity and the Coriolis force must also be considered when determining the torque at a particular joint.
The full set of formulas are presented in the lectures.
Joint-space inertia matrix
Coriolis and centripetal coupling matrix
Gravity loading
Notes: You can see that the fundamental equation for torques is this.
The mass and inertia of the robotic arm
The Coriolis effect is the gyroscopic forces that we need to consider on a joint due to the rotation of other robot joints.
Gravity
The lecture slides go through a very good job at explaining the necessary formulas.